## Slide 1: RC car
Atmega32 Serial communication via Bluetooth
Eng. Mohamed Atef
Software Eng. Ammar Wael

## Slide 2: Introduction
Bluetooth controlled car is a robot which is built using Atmega32 Microcontroller in which serial communication is done via Bluetooth and Programming is done in embedded C language .

## Slide 4
System control :

## Slide 5
Atmega32 Microcontroller
High performance and low power microcontroller
RISC Architecture
Up to 16MIPS throughput 16MHz
2 KB RAM and 1024 Bytes EEPROM
Programmable Serial USART
Programmer friendly

## Slide 6: PIN CONFIGURATION

## Slide 7
What is Bluetooth ?
RF based wireless technology
Low cost
Short range
Less power Consuming
Speed Less than 1Mbps
HC-05
Work modes :
Order-response work mode
Automatic connection work mode

## Slide 8: USART PROTOCOL
Full duplex Asynchronous or synchronous operation
Master or slave synchronous operation
Framing Error Detection
Multi processor communication mode
Double speed Asynchronous communication mode

## Slide 9
RC Car Components in the project
2 Atmega32
3 Bread board
2 Motors
1 Battery slot
HC-05 Bluetooth module
1 HC-SR04 Ultrasonic Module
1 H-bridge

## Slide 10
Microcontroller
1
Microcontroller
2
Bluetooth module
HC -05
Ultrasonic Module
HC-SR04
Dc motor
Led
Dc Steering motor
Buzzer

## Slide 11
DC Motor code :
1.INIT
To initialization the motor
First microcontroller (main)

## Slide 12: 2.DC Motor start control
To start and stop the motor

## Slide 13
3 .DC Motor speed control
To control the speed
*Using timer 0 to control the speed

## Slide 14: 4. DC Motor Direction
To control the direction of the motor
controlled by input 1 &2 in H-bridge
If input (1,0) the direction will be anticlockwise
If input (0,1) the direction will be clockwise

## Slide 15
LED code :
1.INIT
To initialization the LED
By using timer 2

## Slide 16
2.LED LEVEL
To control led Level
Level_0  Led is off
Level_1  Led intensity is ¼
Level_2  Led intensity is ½
Level_3  Led intensity is ¾
Level_4  Led is in full intensity

## Slide 17
Bluetooth module code :

## Slide 18
Ultrasonic code :
Second microcontroller

## Slide 19
From the equation time taken=(timer_overflow_1*256)+ TCNT0
Distance=(time taken *(Sound speed /(float)2000000))/2 in cm
Ultrasonic code :
Using timer 0

## Slide 20
Project Flow chart

## Slide 21
Thank you for your kind attention